## Slide 1: CacheMigrate: Efficient Cache Migration for Load Balancing in Distributed Key-Value Storage Systems
Xianda Meng, Ammar Hawbani, Jiangyuan Chen, Abdulbary Naji, Liang Zhao

## Slide 2: Key-Value Stores
Widely used
  Caching mechanisms
  Real-time analysis and monitoring
  Feature storage for machine learning
Huge scale
  Storing billions of data entries
  Retrieving millions of records with low latency constraints
  Highly load-skewed
Google Data Center

## Slide 3: Existing Solutions
Consistent hashing algorithm
  Ignoring dynamic and skewed workloads
Front-end caching
  Limited cache resources
  Single-rack load balancing cannot meet the needs of multi-rack systems
Data migration and replication
  Service pause during migration
  Incremental migration storage overhead
  Data consistency guarantee

## Slide 4: Caching + Migration = CacheMigrate
Single-rack systems are better suited to caching methods
Multi-rack systems are better suited to migration methods
A
B
A
B
C
C

## Slide 5: Challenges
How to select the right content to migrate
How to minimize service downtime during migration
How to ensure data consistency during migration

## Slide 6: Challenges
How to select the right content to migrate
How to minimize service downtime during migration
How to ensure data consistency during migration

## Slide 7: Load Management & Content Selection
Migration decision:
  The controller monitors the global ToR switch load
Migration start:
  A heavy-hit detector was deployed on the switch to detect hotspots in the network in real time
  Hotspots are stored in the cache and ready for use during data migration.

## Slide 8: Challenges
How to select the right content to migrate
How to minimize service downtime during migration
How to ensure data consistency during migration

## Slide 9: Service Downtime Challenges
Conventional migration may cause:
  Requests reaching outdated server
  Network path inconsistency
  Temporary unavailability while routing converges
Key goal：clients should not perceive any disruption

## Slide 10: Minimizing Downtime via ToR-Level Handling
Switch-based fast rerouting
  KeyMigrationReady → Spine updates routing
ToR temporarily handles all requests (acts as migration proxy)
No client-side retries or REST failures
Rerouting convergence occurs under the switch’s control, not exposed to user traffic

## Slide 11: Challenges
How to select the right content to migrate
How to minimize service downtime during migration
How to ensure data consistency during migration

## Slide 12: Why Consistency Is Difficult During Key Migration
Transition window：
  Source server sending state → new server not ready
  Routing updates are not instantaneous
  Requests might hit different destinations
Potential risks：
  Stale reads
    old value still served by old server
  Lost writes
    updates issued during migration may be dropped
  Read-after-write violations
    write arrives at new server but read goes to old path
DEAD
old path?
new path?
inconsistent version?

## Slide 13: Ensuring Consistency
ToR Cache as a Consistency Barrier
  During routing transition, ToR enters migration mode
  All reads served by ToR cache
  Prevents both source and new server from being accessed
  Ensures a single source of truth for all reads

## Slide 14: Write-Tracking Filter for Migration Writes
Tracks all writes to the migrating key during transition window
Maintains a strictly ordered write log
Prevents write loss or reordering
Ensures RAW, WAW, and WAR correctness
Bloom Filter
KV Cache
1
1
BF
WRITE(A)
MIGRATE(A)

## Slide 15: Final state synchronization
New server finishes receiving migrated state
ToR flushes Write-Tracking Filter in order
ToR exits migration mode and resumes normal routing

## Slide 16: Evaluation
Testbed
  6.5 Tbps Intel Tofino switch
  Commodity servers with ConnectX-5 100Gb.
  Logical partition: 32 spines, 32 ToRs, 32 racks × 32 servers.
  TommyDS; client workloads via YCSB.
  128-bit keys/values.
  Cache per switch: 128 KV pairs.
Baselines
  CacheMigrate(ours),DistCache, NetCache, NoCache
Workloads
  YCSB with Zipf θ = 0.9, 0.95, 0.99

## Slide 17: Result

## Slide 18: Conclusion
Programmable switches enable dynamic migration.
Decouples data movement and query handling.
Ensures 0 downtime, strong consistency.
Large throughput benefit under skew.
Future: more in-network coordination + fault tolerance.
Thank you!